## Slide 1
Project #3413
Sonar Signal Detection and Separation Based on Beam Pattern Analysis
Students: Ariel Jacobson (325553410) | Rom Barat (322911116)
Supervisor: Shaked Sasporta
Location: Israeli Navy Headquarters
Supervisor Approval: ____________
Tel Aviv University | Faculty of Engineering | School of Electrical Engineering

## Slide 2
Introduction & The problem
The Challenge
In a multi-target environment, a loud source (Jammer/Interferer) creates significant energy leakage.
Sonar operators face information overload from multiple sources
The Critical Issue: A quiet target of interest is often completely hidden by the side-lobes of a louder neighbor.
Project Goal
Develop an algorithm for "speaker separation" in sonar context — distinguishing between different sound sources even when they overlap in intensity at a given direction, by leveraging the fact that they arrive from different angles.
Strategic Importance: Reduces operator cognitive load • Faster threat identification • Improved detection of masked targets

## Slide 3
System Requirements & Deliverables
Simulation Environment
ULA sensor array simulation
Delay-and-Sum beamforming
Acoustic propagation model
Configurable SNR & scenarios
Detection Algorithm
ML-based target detection
Target vs. noise classification
Target counting algorithm
Spectral feature extraction
Separation Output
Separate audio per target
Spatial masking removal
Adaptive null-steering filter
Clean playback for operator
What Are We Simulating
We are building a Data Factory to train a Neural Network. The simulation replicates the exact physics of masking:
  Scenario: A target enters through the "Side Lobe" of a Jammer.
  The Problem: Conventional math cannot distinguish the target from the Jammer's leakage.
  The Expectation: By generating thousands of these "impossible" scenarios, the model will learn the unique fingerprint of the array's side-lobes and filter them out.

## Slide 4
System Architecture
Acoustic
Input
Sensor Array
(ULA)
→
Spatial
Filtering
Delay-and-Sum
Beamforming
→
Spectral
Analysis
Welch / BT
PSD
→
ML
Detection
Counting and Seperation
→
Separated
Audio (optional)
Per-target
channels
Implementation Details
Spatial Filtering (Beamforming)
Uniform Linear Array (ULA) with 100 sensors
Delay-and-Sum algorithm with phase shifts
DOA scanning: -90° to +90°
Sub-sample delay via frequency domain
Detection & Separation (Planned)
SVM as baseline classifier
Neural network for improved accuracy
Spatial features + spectral features as input
Adaptive null-steering for separation

## Slide 5
Stage 1: Spatial Filtering (Beamforming)
Key Observations
Main lobe steered to 30° (target direction)
Side lobes attenuated by ~13 dB
Jammer at 20° experiences ~20 dB attenuation
Polar view confirms directional selectivity
Physics Engine
Time delay based on angle θ
Phase-shift in frequency domain for precision

## Slide 6
Stage 2: Spectral Estimation Methods
Method Comparison
1. Periodogram
High variance, hard to detect
2. Bartlett
Reduced variance, lower resolution
3. Welch ✓
Best SNR, clear 1200Hz peak
4. Blackman-Tukey ✓
Smoothest, ideal for counting
Selection: Welch's method for detection (lowest MSE) | Blackman-Tukey for visualization (smoothest curve)
Target at 1200 Hz clearly visible with Welch & Blackman-Tukey, while Periodogram shows only noise fluctuations

## Slide 7
Simulation Pipeline Demo
Step 1: Audio Loading
1-second normalized vessel signal (8000 samples)
Step 2: Controlled Noise Injection
White Gaussian noise at SNR = 10 dB
Zoomed view reveals the "jitter" on the signal
Step 3: Sensor Array Simulation
100 sensors receive delayed copies of signal
Diagonal stripe = wavefront propagation
~140 sample delay between Sensor 0 and 99

## Slide 8
Multi-Target Detection Demo
Single Vessel at 30°
Two Vessels at -30° and 20°
Key Results
Beamgram (Panel A): Time-angle energy map shows concentration at target directions
Spatial Spectrum (Panel B): Clear peaks at both target angles (-30° and 20°)
Polar View (Panel C): Directional energy confirms successful spatial filtering

## Slide 9
Current Status & Progress
Completed
✓ Theoretical background study
Acoustics, beamforming, spectral methods
✓ Simulation environment (Python)
ULA model, physics engine, beamformer
✓ Spectral estimation comparison
Selected Welch & Blackman-Tukey
✓ Multi-target scenario demonstration
Successfully generation a number of vessels at different angles
✓ Dataset generation
Synthesizing training data for ML models
In Progress
◐ ML detection algorithem
Target vs. noise binary classification
○ Target counting algorithm
Estimating number of active sources
○ Audio separation output
Generating per-target audio channels
Technology Stack
Python | NumPy / SciPy (signal processing) | Matplotlib (visualization) | Scikit-learn / PyTorch (ML - planned)

## Slide 10
Project Timeline
Milestone | Target Date | Actual Date | Notes
Theoretical background study |  |  | Completed
Simulation environment |  |  | Completed
Dataset generation | 30/12/2025 |  | Completed
Basic detector (Detection) | 23/01/2026 |  | In progress
Mid-project presentation | Feb 2026 |  | 
Target counting algorithm | 20/03/2026 |  | 
Audio channel generation | 20/04/2026 |  | 
Stress testing | 05/05/2026 |  | 
Final report | 24/05/2026 |  | 
Final presentation & poster | 23/06/2026 |  |